## Slide 1: ENGI 301 SpotiBox Proposal
2/25/2024
Cameron Erber

## Slide 2: Background Information
Music is a medium that directly influences mood and can transport you to another world. To accentuate the experience that music provides, additional senses can be included. A main sense that has been focused on with success is the creation of a visual complement to the audio. A device can be constructed to create a visual representation
  in essence, a music “visualizer”

## Slide 3: Device Proposal
A dedicated desktop music visualizer with Spotify integration
  Builds off of previous ENGI 301 project “TICKER” by Robert Heeter
    Project/code: https://www.hackster.io/rcheeter/ticker-led-matrix-widgets-via-wifi-with-a-pocketbeagle-edd915
Added features
  Realtime music visualizer
    Based on audio frequency composition, tempo, “tatums”, and loudness from Spotify API
  Color matching of visualizer and device UI with album art
  Auto-brightness (light sensor)

## Slide 4: System Block Diagram
PocketBeagle
GPIO
GPIO
Shift Register
1
Shift Register
2
LED Matrix Left
LED Matrix Right
USB Breakout
USB1
USB Wifi adapter
VIN
Power button
Red A
Blue A
Clock
Select A
Select C
Red B
OE
Red A
Blue A
Clock
Select A
Select C
Red B
OE
Green A
Latch
Select B
Select D
Green B
Green A
Latch
Select B
Select D
Green B
5V Power adapter
GPIO
Play/Pause/Skip/Rewind
Light sensor
I2C1
SCL
SDA

## Slide 5: Power Block Diagram
PocketBeagle
VOUT
3.3 V
Shift Register
1
Shift Register
2
LED Matrix Left
LED Matrix Right
USB Breakout
USB1
USB Wifi adapter
VIN
Power button
5V Power adapter
5V
5V
Ground
Ground
5V
Ground
5V
Ground
5V
3.3V
Ground
Ground
Ground
Ground
Ground
Ground
GPIO
Play/Pause/Skip/Rewind
Light sensor
I2C1

## Slide 6: Components / Budget
Component | ENGI301 to Buy? | Cost
PocketBeagle | N/A | N/A
64x32 RGB LED Matrix - 4mm pitch https://www.adafruit.com/product/2278 | Yes | $39.95
Adafruit BH1750 Light Sensor https://www.adafruit.com/product/4681 | Yes | $4.50
Adafruit 5V / 4A Power supply wall adapter https://www.adafruit.com/product/1466 | Yes | $14.95
TP-Link USB Wifi Adapter https://a.co/d/ig5AckR | Maybe | $9.99
TXS0108E Level Shifter 3.3V / 5V (5 Pack) https://a.co/d/a8qwK6o | N/A | N/A
Female DC Power adapter - 2.1mm jack to screw terminal block https://www.adafruit.com/product/368 | N/A | N/A
RR511D1121 On/off rocker https://www.digikey.com/en/products/detail/e-switch/RR511D1121/2116256 | N/A | N/A
Press button | N/A | N/A
USB Type A Female Breakout | N/A | N/A
N/A = already have / from OEDK

## Slide 7: Software
Main points of action:
Power on
Main class
  Set display brightness  brightness class
    Brightness class
      Convert sensor output to RGB brightness level and output
  Set welcome display
  Initialize spotify token access  spotify_initializer class
    Try request access token  if failed, get new and repeat
  Display music visualizer  visualizer class
    Get track title / album art and display
    Get song data, perform fft and display
  Button
    Always waiting for button press
      Single press  play song if paused or pause song if playing
      Double press  skip song
      Triple press  previous song

## Slide 8: SW Flow Diagram
Power on
Set Welcome Display
Main class
Spotify initializer
Display Brightness
Display brightness class
Spotify initializer class
If false
Visualizer
Receive light sensor output
Convert to LED matrix brightness
Update LED matrix brightness
Request access token
Check access token
After 1 hr
If false
Request current song data
Display track title
Display track art
Get track audio data
Perform FFT
Display waveforms
Visualizer class
Every song
Set brightness
Button pressed
Button press
Skip song
Single press
Double press
Song playing
Song paused
Play song
Pause song
Previous song
Triple press